## Slide 1: MySynth
Final prototype demonstration audio effects module

## Slide 2: Some history.
First idea: ARM Cortex-M MCU
To slow CPU
No audio processing libraries
Complex to develop and debug
Final idea: Raspbery Pi and Linux
”Powerfull” CPU
Well documented open source audio libraries
Use ALSA and PulseAudio to abstract from audio hardware

## Slide 3: Implementation details.
ALSA (Advanced Linux Sound Architecture) Allows to abstarct from audio hardware. Module will works with any soundcard, if it has Linux driver.
The Synthesis ToolKit in C++ (STK) https://ccrma.stanford.edu/software/stk/ Open source audio processing library, well documented, very easy to integrate to the project as Linux library.

## Slide 4: Effect list
Frequency filters (three low-pass filters, two band-pass filters and one high-pass filter).
Delay blocks ("echo" effect).
Modulators (one "vibrato" effect which multiply incoming audio signal and sinusoidal wave)
Non-linear blocks ("distortion" effect) By combining this 4 basic blocks every effect can be implemented, we can have in real synthesizer. Here we demonstrate that our program is capable of doing everything what is may be required by end user.

## Slide 5: https://github.com/AlekseiGimbitskii/MySynth_ELT-23056
Do audio processing in C++
Use Linux ALSA
Utilize STK library (open source audio processing library)
Run Python code from C/C++ program
If you are curious of something from this list or will need to do it in future, feel free to visit our GitHub repository and use our code as refercence.